## Slide 1: Combination Circuits

## Slide 2: Combination circuits
Combination or mixed circuits contain both series and parallel connections

## Slide 3: Applying Kirchhoff’s Voltage law to a mixed circuit
To analyze a mixed circuit, start by separating the circuit into sections that are connected in parallel and sections that are connected in series.

## Slide 4: Applying Kirchhoff’s Voltage law to a mixed circuit
To view a mixed circuit, start by separating the circuit into sections that in series and sections that are connected in parallel.
Parallel Circuit
Series Circuit

## Slide 5
Using this approach of two separate paths, you can think of two independent series circuits.
Source = 40 V, lamp 1 = 10 V, lamp 3 = 20 V.
Find the voltage of lamp 2 and 4.
Lamp 1
Lamp 2
Lamp 4
Lamp 3

## Slide 6
Use KVL to solve for V2
What formula do we need to use?
Vsource = V1 + V2 + V3
40 V = 10 V + V2 + 20 V
40 V = 30 V + V2
V2 = 10 V

## Slide 7
Use KVL to solve for V4
According to KVL, voltages in a parallel circuit are the same. Thus V3 must equal V4
Vsource = V1 + V2 + V4
40 V = 10 V + 10 V + V4
40 V = 20 V + V4
V4 = 20 V

## Slide 8: Applying Kirchhoff’s Current Law to a mixed circuit
The current in a series circuit is constant and stays the same as the source current. The current in a parallel circuit is divided along the paths.
Isource = 0.40 A
I3 = 0.10 A
Find I1 and I2
Lamp 1
Lamp 2
Lamp 4
Lamp 3

## Slide 9
What is the formula for current in a series circuit?
Iseries = I1 = I2
0.40 A = I1 = I2
Therefore I2 = 0.40 A

## Slide 10
The amount of current entering a junction is equal to the amount of current exiting a junction.
What is the formula used to find current in a parallel circuit?
Iparallel = I3 + I4
0.40 A = 0.10 A + I4
I4 = 0.30 A

## Slide 11: Resistance in a mixed Circuit
Calculate the equivalent resistance for the circuit diagram below
R5 = 18 Ω
R4 = 30 Ω
R3 = 50 Ω
R2 = 75 Ω
R1 = 12 Ω

## Slide 12: Resistance in a mixed Circuit
Step 1. Divide the circuit into series and parallel parts.
R5 = 18 Ω
R4 = 30 Ω
R3 = 50 Ω
R2 = 75 Ω
R1 = 12 Ω
Parallel

## Slide 13: Step 2. Find the equivalent of the parallel part of the circuit.

## Slide 14
Rparallel = 15 Ω

## Slide 15: Step 3. Redraw the circuit using the equivalent resistance from step 2.
R5 = 18 Ω
Rparallel = 15 Ω
R1 = 12 Ω

## Slide 16: Step 4.
Solve to determine the equivalent resistance of the remaining series circuit. Let the equivalent resistance for the complete circuit be Rtotal :
What is the formula to calculate resistance in a series circuit
Rtotal = R1 + Rparallel + R5
Rtotal = 12 Ω + 15 Ω + 18 Ω
Rtotal = 45 Ω
Therefore, the equivalent resistance is 45 Ω

## Slide 17: Questions
What is the total resistance of the mixed circuit shown to the right, note that each resistor has a resistance of 5.0 Ω. T (4)
R1
R3
R4
R5
R2

## Slide 18: Questions
What is the total resistance of the mixed circuit shown to the right, note that each resistor has a resistance of 5.0 Ω. T (4)
R2
R3
R4
R1
R5

## Slide 19
Draw the following circuit and calculate the unknown in each situation. C (1)
  A 6.0 Ω resistor (R1) is in series with a power source, two more resistors (R2 = 20 Ω and R3 = 30 Ω) are in parallel to each other and in series with R1. T (2)
  If the power source was 9.0 V, what is the voltage drop across each resistor? T (3)