## Slide 1: Electric Current and Circuits

## Slide 2: Electric Current
Electrons in a static state have energy, but are far more useful when they are made to transfer their energy. Electric current involves electrons repelling one another and passing through a conductor.
The flow of electric charge is called electric current.

## Slide 3: Current
Current is the rate of charge flow and is given the symbol I. Current is the total amount of charge moving past a particular point in a conductor divided by the time taken.

## Slide 4: Current
Charge
Time

## Slide 5
I is the current in amperes (A)
Q is the charge in coulombs (C)
t is the time in seconds
One ampere is one coulomb of charge moving past a particular point in a conductor every second. A = C/s

## Slide 6: Example 1
How much current flows through a hair dryer if 1400 C of charge pass though it in 2.25 min?
Q = 1400 C
I = ?

## Slide 8
I = 10.4 C/s
Therefore, the current through the hair dryer is 10.4 A.

## Slide 9: Example 2
A night light uses a 7 W light that draws about 6.0 x 10-2 A of current. How much charges passes through this bulb in 8.0 hours.
I = 6.0 x 10-2 A
Q = ?

## Slide 11
Q = 1.7 x 102 C
Therefore, the charge through the light bulb is 1.7 x 102 C

## Slide 12: Example 3
How many electrons have passed through the night light in example 2. The charge on one electron is 1.602 x 10-19 C.
Q = 1.7 x 102 C
e = 1.602 x 10-19 C
N = ?

## Slide 14
N = 1.1 x 1021 electrons
Therefore, 1.1 x 1022 electrons will have passed through the night light in 8 hours.

## Slide 15: Direction of Current Flow
Historically, current was thought to flow from positive (+) terminal to the negative (-) terminal of any supply unit. The model of positive charge flow is called conventional current and is still used today.

## Slide 16: Direction of Current Flow
For this class we will think of electrons from the black negative (-) terminal to the red positive (+) terminal.

## Slide 17: Measurement of current
An Ammeter (a current measuring device) must be wired so that all current flows through it. The ammeter must be an excellent conductor so that no energy is lost due to its addition to the circuit.

## Slide 18
In DC or direct current, the current flows in a single direction from the power supply through the conductor to a load, such as a light bulb, and back to the power supply.

## Slide 19
In AC or alternating current, the electrons periodically reverse the direction of flow.

## Slide 20
In order for electric current to flow, it must have a complete path from the negative side of the power supply to the positive side. The path of electric current is called a circuit.

## Slide 21: Drawing circuits
Engineers and designers of electrical circuits use special symbols that show the components and connections in a circuit.
A drawing made with these symbols is called a circuit diagram.
Follow these rules when you draw circuit diagrams.
Always use a ruler to draw straight lines for the conducting wires.
Make right-angle corners so that your finished diagram is a rectangle.

## Slide 22: Electric Circuit Diagrams and Symbols
Conductor or wire
  To pass current very easily from one part of a circuit to another.

## Slide 23: Electric Circuit Diagrams and Symbols
Cell-Supplies electrical energy
  The positive end is bigger than the negative end.

## Slide 24: Electric Circuit Diagrams and Symbols
2 Cells
Note: every time a cell is added you need to draw another cell.

## Slide 25: Electric Circuit Diagrams and Symbols
DC Source- Electrical energy source
  DC = Direct current, always flows one way

## Slide 26: Electric Circuit Diagrams and Symbols
AC Source - Electrical energy source
AC = Alternating current, continually changing direction

## Slide 27: Electric Circuit Diagrams and Symbols
Ground –
  A connection to earth

## Slide 28: Electric Circuit Diagrams and Symbols
Switch - An on-off switch allows current to flow only when it is in the closed (on) position

## Slide 29: Electric Circuit Diagrams and Symbols
Lamp
  A transducer which converts electrical energy to light

## Slide 30: Electric Circuit Diagrams and Symbols
Resistor
  A resistor restricts the flow of current,

## Slide 31: Electric Circuit Diagrams and Symbols
Ammeter
  -Device that measures current
A

## Slide 32: Electric Circuit Diagrams and Symbols
Voltmeter
-Device that measures voltage
V

## Slide 33: Electric Circuit Diagrams and Symbols
Motor -electrical load that converts electrical energy into movement
M